## Slide 1: Project „Escape Room“
Group 4 – Doors and first puzzle
David, Mario, Sarah

## Slide 2: Interactions
open
RIGHT

## Slide 3: Interactions
close

## Slide 4: How does this communciation work? -> MQTT
Server
Door 2
Door 1
Globes
open/close
Activated/
inactivated
Touched/
not touched
open/close
open/close
solved
Activated/inactivated
Puzzle

## Slide 5: Puzzle
Components:
16x2 IC2 LCD Display
4x4 Matrix Keypad
3D printed housing
Microcontroller:
ESP32
Communication between microcontroller and components:
I2C Interface to LCD display
Analog Inputs to Keypad

## Slide 6: Puzzle
Initialisation
Right password entered?
no
Send via MQTT: Puzzle solved -> Door will open
yes

## Slide 7: Doors
Mechanical components:
Mounting
Gearbelts
Gearwheels
Floor guide rail
Endstops
Electrical compnents:
Motor and Driver
Endstops switches
Voltage supply
Microcontroller:
- ESP 32

## Slide 8: Doors
Mechanical components:
Mounting
Gearbelts
Gearwheels
Floor guide rail
Endstops
Electrical compnents:
Motor and Driver
Endstops switches
Voltage supply
Microcontroller:
- ESP 32

## Slide 9: Doors – Functional principle
Get command: „open“
Get command: „close“
Initialisation
Slowly move door in one direction
Endstop
touched?
no
yes
Repeat some for other side
Save Endpositions
Move the door to the respective end stop
Move the door to the respective end stop
Send MQTT message: open
Send MQTT message: closed

## Slide 10: Plasma Globes – Sensing touch events
touched
touched
touched

## Slide 11: Plasma Globes - Puzzle
close
open
touched/ not touched
closed!
open/close
touched/ not touched
touched/ not touched
master
slave
slave
slave